## Slide 1: Using Xilinx Vivado for SDR Development
Laurence Barker G8NJJ

## Slide 2: Contents
What’s in an HF SDR FPGA?
Creating a DSP TX design with Vivado IP Integrator
Debugging DSP TX using the simulator
Running On Hardware

## Slide 3: What’s my ambition?
I want to understand HF SDR algorithms
I want a radio where I have written some of the code
I want to re-discover FPGA design after 25 years
This will take several years… I’m only 3 years in
I’ve done nothing original – just learned from others
  Pavel Demin (Red Pitaya)
  Phil, VK6APH and Warren Pratt, NR0V and others (HPSDR)
Notes: The last bit may belong on a different slide

## Slide 4: What’s in an HF SDR project?
Powersdr
pihpsdr
Notes: At the left – conventional broadband RF
Data conversion covering the whole HF band. 60MHz b/w 14 or 16 bits
Then PC processing with the user interface. Many choices of app available. This is where most of the complexity is!
And if you want it you can still have a conventional front panel with tuning knob, controls and pushbuttons

## Slide 5: One way to make this – Red Pitaya
Image copyright Red Pitaya d.d
Notes: Lots of ways to make SDR.
One way – The RedPitaya
Uses ZynqSystem on Chip FPGA combining ARM processing & FPGA

## Slide 6: Another Way – System on Module
Ultra96
Images copyright Avnet Inc
UltraZed-EG
Notes: Another way – think of it as a single board computer connected to ADC/DAC

## Slide 7: What’s in a System on Chip FPGA?
Two halves, one chip
Processing System (PS)
  ARM processors
  SBC-like I/O
  SDRAM interface
Programmable Logic (PL)
  Configurable Logic
  DSP Slices
  Dual port RAMs
Programmed differently!
Processing System
Programmable Logic
2/4 core ARM
Logic
Memory
DSP
Processor I/O
USB, DisplayPort,
Serial,
I2C,
GPIO…
SelectIO
For ADC, DAC, T/R, Codec…
C, Python, …
VHDL, Verilog…
ZU3EG: quad core ARM;
2.3M equivalent gates +950KB RAM + 360 DSP slices
Notes: Lots of different devices available from both Intel and Xilinx
Xilinx Zynq & Ultrascale+ Zynq families

## Slide 8: Overall Design Flow - Xilinx
For an SBC - This might be done for you
SDR App
Linux Operating System
FPGA
SD Card
Vivado
Your Design
“normal” GCC / GDB
petalinux-create
root fs, FSBL
Exe file
boot.bin
petalinux-build
petalinux-package
.xsa file
Image copyright Avnet Inc
Notes: 3 quite different technologies
“app” uses conventional software tools eg Gnu C compiler
Linux – you need a kernel, drivers and a root filesystem. Xilinx Petalinux tools will help create these (and SBC supplier may have helped too)
FPGA – Vivado creates the FPGA design file. (simple merge process with the petalinux boot loader too)
Everything goes on an SD card into your SBC

## Slide 9: 3 ways to Design the FPGA
Write VHDL or Verilog code by hand
  A lot of effort
Use someone else’s IP, and join it together
  Re-using good designs
  This is what we will be doing today
Synthesis from a higher level language (eg C, python, MATLAB, GNU radio)
  Could be the way of the future?
  Eg port bits of Warren Pratt’s WDSP?
IP = Intellectual Property

## Slide 10: HF SDR: What needs to happen the FPGA
PC interface
ADC
Digital Oscillator
Mixer
Low pass Filter
Low Pass Filter
Sample rate 122.88MHz
Sample rate 48KHz
(or multiple)
Decimate (Divide clock) by 2560
14.205MHz
14.200MHz
5KHz
Inphase
Quadrature
14.205MHz
sin, cos
0 ± 24KHz
2560
2560
TX is the same thing, backwards
Notes: Quite a simple process
Mix the signal with sin, cosine of local oscillator
Filter and reduce the sample rate
Send data to PC

## Slide 11: The DSP Blocks needed
CIC filter
FIFO
Memory
(First in, First Out)
ADC
Direct Digital Synthesiser
Complex Multiplier
FIR Filter
FIR Filter
Sample rate 122.88MHz
Sample rate 48KHz
(or multiple)
Decimate (Divide clock) by 2560
Inphase
Quadrature
sin, cos
CIC filter
TX is the same thing, backwards
Decimate by 384
Decimate by 8
Low pass filter 0-22KHz
Notes: Quite a simple process
Mix the signal with sin, cosine of local oscillator
Filter and reduce the sample rate
Send data to PC

## Slide 12: Useful Information
Please read these first!
  Xilinx UG995: Designing IP Subsystems Using IP Integrator (Tutorial)
  Xilinx UG994: Designing IP Systems Using IP Integrator (User Guide)
Other useful information sources
  Every IP core has a datasheet
  Xilinx PG085 AXI4-Stream Infrastructure IP Suite v2.2 (data sheet)
  “The ZYNQ Book” by Louise Crockett, Ross Elliot, Martin Enderwitz & Robert Stewart

## Slide 13: Downloading & Installing Vivado
Webpack edition – free to use, for smaller devices
2-3 releases per year – current is 2019.2
  Your design belongs to that version, until you upgrade
  You could need 2 or 3 versions installed, ~50GByte each!
Decide how/where to run
  Vivado – x64 Windows PC
  petalinux tools – in a ubuntu VM on the PC
Create a Xilinx account, then
Download & run Xilinx Unified Installer 2019.2: Windows Self Extracting Web Installer then select Vitis, and no licence manager

## Slide 14: Vivado Main Screen
Main Design Steps
Source files
Project information

## Slide 15: IP Integrator
We will be using the IP Integrator in Vivado
Xilinx creates the IP
We join it together in a block diagram
3 reasons why that’s good:
  It’s quick to learn
  The code works
  Many others in the design team can understand the diagram

## Slide 16: Starting an IP Integrator design
Click “Create Block Design”
You get a design canvas
Just like a schematic editor
Add IP blocks (predesigned cores)
Add modules (Verilog or VHDL code)
Create ports for input and output
Join together with wires

## Slide 17: Intellectual Property (IP) Cores available
Around 180 IP cores available
  Processors
  DSP
  Video, display drivers
  Interfaces
  Infrastructure
Standardised interfaces
  AXI4-Bus
  AXI4-Stream
DSP includes:
  Complex Multiplier
  DDS Compiler
  CIC Compiler
  FIR Compiler
  2G/3G/4G cores
  Fast Fourier Transform
  Memory, FIFO

## Slide 18: Look at the I/O for a “typical” FIR filter block
Input: a stream of input samples
Output: a stream of output samples
It decimates (reduces) the data rate
The data in and out are AXI4-Stream
  A standard way of passing streams of samples
This makes it really easy
  Join the blocks, and they sort out the data rates
You need to understand it a bit!
Slave (input) data
Master (output) data
Clock

## Slide 19: AXI4-Stream – “Glue” for all the DSP blocks
A stream of data from one source (master) to one destination (slave)
  tdata: A “pipe” of samples, N bytes wide
  tvalid: A signal from the master to say “I have data to transfer”
  tready: A signal from the slave to say “I am ready to accept data”
All devices are clocked at the same speed
  tready and tvalid cause the data to flow when ready
Data transfers when both tready and tvalid are 1
Just join the blocks…
They work out when to transfer data

## Slide 20: Add the DSP blocks that we need
Double click them to get the configuration page

## Slide 21: Local Oscillator DDS Configuration(1)
Double click a block to edit its settings
The DDS has 4 pages of settings!
Configuration Tab
  System Clock 122.88MHz
  Spurious free dynamic range 96dB
  Frequency resolution 0.4Hz
Implementation Tab
  Set to streaming
  untick “has phase out”

## Slide 22: FIR Filter Datapath
The FIR filter has a slow sample rate (384KHz) & could run much faster
And it uses a lot of resources
To be efficient: we multiplex both I/Q streams through the same FIR
For this Xilinx provides the AXI4-Stream Data Width Converter1
1: see Xilinx AXI4-Stream Infrastructure IP Suite v2.2 (PG085) p14

## Slide 23: FIR Filter Datapath
Slave interface TDATA width 4 bytes
Master interface TDATA width 2 bytes
1: see Xilinx AXI4-Stream Infrastructure IP Suite v2.2 (PG085) p14
Slave interface TDATA width 3 bytes
Master interface TDATA width 6 bytes

## Slide 24: FIR Filter – calculate the coefficients
We need to design a filter
Run tfilter1 online
Passband 0-22KHz, 0.2dB ripple
Stopband 24-384KHz, -140dB
Copy out the coefficients as double precision
Use a spreadsheet to change format to .coe2
1: http://t-filter.engineerjs.com/
2: https://www.xilinx.com/support/documentation/sw_manuals/xilinx11/cgn_r_coe_file_syntax.htm

## Slide 25: FIR Filter Configuration
Interpolating filter, by 8
2 channels
Clock frequency 122.88MHz, input rate 48KHz
Input data 16 bits, o/p data 20 bits
Coefficient width 22 bits
Output tready ticked
Filter taps in coefficient file (.coe)

## Slide 26: CIC Filter Configuration
We have 2 identical CIC filters
6 stages
Interpolate by 320
Input width 20 bits, output width 23 bits
Output tready ticked

## Slide 27: Join the blocks together… DSP finished!
We’ve done the Maths
  All Xilinx IP
We need to little “glue” to finish off
I/Q audio in here
FIR filter
CIC filters
Complex multiplier
DDS
Connect DAC here
VFO Frequency word here
Clock and reset for everything

## Slide 28: Connect the DAC
Add an output port to the schematic
  Allows the signals to be I/O pins & to be accessed in the simulator
Click the + on the master axi4-stream output
  Now you can connect to the tdata bus
Add a slice IP core to rip 24 bits from the 48 bit I/Q bus
Use “create port” to make this

## Slide 29: Setting the DDS Frequency
I’m going to feed in a constant value to test this
Data needs to become an axi4-stream
I’ve created “bus_to_axis” Verilog (only 48 lines)
Right click “add module” & select “bus_to_axis.v”
Double click & set “Validonchangeonly” to 0
16 bit constant bus
From a port
AXI4-stream with same data value

## Slide 30: Feeding in I/Q TX Audio
Will normally come from the ARM cores, via a FIFO
Will take too long to bring a processor into this talk!
For now, just use another DDS
Set DDS properties:
Clock rate 48KHz
Output frequency fixed, 10KHz
Has output tready (v important!)

## Slide 31: Providing clock and reset
For a hardware test – clock and reset would be external signals
You can create clock and reset in the simulator, every time
But Xilinx provides a simulation source
Provides a simulated clock and reset signal
Set its properties:
Clock frequency 122880000Hz
Reset: active low, 200 clocks

## Slide 32: Now we’re ready to Simulate
Save and close the block design
Create an HDL wrapper
Select “Run Simulation”
….and almost certainly it won’t work
My approach has been: break into small sections and test each
Include debug until it is all working
Let’s break down this down into sections

## Slide 33: Behavioural Simulation Basics
This is how you debug – you have access to everything
To view signals, create ports on the block design
To view a signal
  drag it from the list at the left
To set a value on an input
  Right click and select “force constant”
To run and stop the simulator
  run and pause buttons on main toolbar

## Slide 34: Simulating the DDS
Start with just the DDS, & Verilog module
Route its outputs to ports
(use “slice” to split into 2 16 bit buses)
Run “behavioural simulation”
  Drag your two 16 bit buses onto screen
  Set waveform style to analogue
  Set radix to signed decimal
  Set frequency word to 0042AAAA
And we get 1MHz I, Q sinewaves

## Slide 35: Add the complex multiplier
Connect complex multiplier to DDS
Add another DDS, constant frequency 0.5MHz
Connect the ports to complex output
And we get 1.5MHz I, Q sinewaves

## Slide 36: Add the Filter Chain
Break to smaller chunks or add debug outputs as needed
Moved the I/Q test DDS to here
Now set to 10KHz

## Slide 37: Simulating the filter chain
First – simulate to see the modulation signal
Set VFO DDS to 0Hz
Be patient…
  The I/Q filters take ~2ms to settle
  Several minutes on my PC!
We see 10KHz sinewaves
  As expected

## Slide 38: And the modulated output
Pause the simulation
Force DDS frequency word to 0x0042AAAA (1MHz)
Continue the simulation
Now we see the modulated carrier
1.01MHz
Zoomed in – 1MHz sinewave

## Slide 39: That’s your TX - connect to a DAC?
Convert the output word to binary
  I’ve used a tiny bit of Verilog
  (You only need to invert the top bit)
  Connected 8 bits out to an R-2R resistor ladder “DAC”
We need a real clock and reset
  Can get that from the ARM cores in my Xilinx device
  Use a PLL clock multiplier to get 122.88MHz
  (OK for testing, not for a radio!)
Assign the pins, then generate bitstream
Use JTAG to download to the FPGA

## Slide 40: And here is the output waveform
Not bad from a DAC made from resistors!
1.01MHz, as expected

## Slide 41: Summary
We’ve scratched the surface, at least
  Made a simple TX
  Simulated it
  And run it on an FPGA
Adding a receiver is the same thing, but the other way round
Still need “glue” to connect to the processors
And I still need to master the Linux bit!